CSPCWG1-8C

# Proposal for ADDITION TO AN EXISTING  work item

Pilot Boarding Areas

# Submitted by Australia 3 August 2004

| Executive Summary: | It is proposed that in the review of M-4, section B-400, consideration be given to incorporating B-491.1 and B-491.2 into one section and adding a paragraph on pilot boarding areas. |
| --- | --- |
| Actions to be taken: | Consider Australia’s suggestion at CSPCWG1 meeting in November and agree to proposed method of portraying such areas in principle. Final wording to be discussed and decided when review of section B-400 is carried out in due course. |
| Related Documents: | M-4, B-160, B-491.1, B-491.2, INT1 IT 1.1, S-57 (Ed 3.1) Appendix B.1 Product Specification for ENC, Edition 2.0, table 3.1, S-57 Appendix B.1 Annex A – Use of the Object catalogue for ENC, Edition 2.1, section 13.1.2. |

## 1.	Introduction / Scope

Australia has been informed of a pilot boarding area, which needed to be charted.  M-4 currently does not include any guidance on portraying such areas, so the issue is raised in accordance with M-4 B-160 and CHRIS15-5B-rev2.

## 2.	Analysis / Discussion

S-57 (Ed 3.1) Appendix B.1 Product Specification for ENC, Edition 2.0, table 3.1 permits pilot boarding places (PILBOP) to be either points or areas.  As we now have an actual example of an area, it is suggested that the specifications for paper charts should be amended to provide advice on how to portray pilot boarding places as areas.  Procedures have been adopted within our HO and proposed additions for the relevant sections are attached for M-4, however it is also suggested that an example of an area should also be added to INT1. S-57 Appendix B.1 Annex A – Use of the Object catalogue for ENC, Edition 2.1, section 13.1.2 does not include any particular guidance for encoding area PILBOPs but the symbology is taken care of by S-52 for ECDIS.

## 8.	Target Completion Date

To be determined.  Low priority.  It is suggested that this addition could be reviewed together with the future review of B-400 that is already a work item for the CSPCWG (task A.4).

## 10.	Action Required

Discuss proposal at CSPCWG meeting No 1 in November.  The annex includes the proposed wording for addition to M-4.

Annex to CSPCWG 1-8C

M-4 §B 491.1	The position of a pilot cruising vessel:

Add the following paragraph at the end of the section:

In some cases, the position of a pilot cruising vessel is defined as an area.  Where such an area has been defined, covering one square nautical mile or larger, the limit shall be charted using a magenta dashed line (INT1 – IN 1.2) on charts of scale 1:300000 and larger.  The legend ‘Pilot Boarding Area’, in 7 pt Medium U/L Italic Magenta text, should be charted within the limits.  Where the chart scale does not permit the insertion of the legend within the area, a pilot boarding place symbol (INT1 – IT 1.1) should be inserted within the area.  If considered necessary, a cautionary Note may be inserted in magenta near the title, to provide additional information about the area.

M-4 §B 491.2	The position of a meeting (boarding) place:

Add the following paragraph at the end of the section:

In some cases, the position of a meeting (boarding) place is defined as an area.  Where such an area has been defined, covering one square nautical mile or larger, the limit shall be charted using a magenta dashed line (INT1 – IN 1.2) on charts of scale 1:300000 and larger.  The legend ‘Pilot Boarding Area’, in 7 pt Medium U/L Italic Magenta text, should be charted within the limits.  Where the chart scale does not permit the insertion of the legend within the area, a pilot boarding place symbol (INT1 – IT 1.1) should be inserted within the area.  If considered necessary, a cautionary Note may be inserted in magenta near the title, to provide additional information about the area.