CSPCWG3-9.1.1A

3rd CSPCWG MEETING

Monaco, 22-24 November 2006

## Paper for Consideration by CSPCWG

## Draft specifications for DGPS station

| Submitted by: | UK |
| --- | --- |
| Executive Summary: | CSPCWG2 approved a new symbol for DGPS. This was subsequently endorsed by IHO Member States. |
| Related Documents: | CSPCWG2 record. IHO CLs 30 & 48/2006 |
| Related Projects: | On-going revision of M-4 |

## Introduction / Background

Extract from CSPCWG2 record:

8.8 Charting of Differential GPS stations (ES)

The WG discussed the value of charting DGPS stations and it was agreed that DGPS stations may be charted if required, by use of the magenta radio circle with associated upright legend DGPS, ie as German national symbol Sa.

It was agreed that INT 1 S51 was the appropriate place for the new symbol. Chairman and Secretary would review the options for the placement of an associated specification in M-4.

ACTION 23: Secretary to draft CSPCWG Letter to WG members, TSMAD and C&SMWG, re proposal for DGPS stations, and include suggested placement of specification in M-4.

The new symbol was approved by IHO Member States following consultation by IHO CL 30/2006. Confirmation was given by IHO CL 48/2006. The symbol will be added to INT 1 as described in due course.

## Recommendations

  - There remains a need to include specifications for the new symbol (as it has been agreed that all INT symbols should have related entries in M-4). The CSPCWG Secretary has therefore drafted a specification below, to be located in M-4 as stated in Annex B to IHO CL 30/2006.

B-481.5		The use of radiobeacons for data transmission, eg Omega corrections and meteorological information, is not at present indicated on charts. [existing text to be deleted] Differential Global Positioning System (DGPS) is an enhancement to the Global Positioning System that uses a network of fixed ground-based reference stations to broadcast the difference between the positions indicated by the satellite systems and the known fixed positions.

DGPS stations that provide DGPS corrections to the mariner must be charted, if required, by the magenta radio circle with associated upright legend DGPS:

Insert symbol	 S51

## Action Required of CSPCWG

  - The CSPCWG is invited to discuss and endorse the draft specification.