Red-Line Version

B-122.1

International Abbreviations

.	.	.

.	.	.

.	.	.

M

m	Medium	J 31

m	Metre(s)	B 41, P 13

m	Minute(s) of time	B 50

M	Mud	J 2

M	International Nautical mile(s)
(1852 m) or sea mile(s)	B 45, P 14

Man	Manually activated	P56, R2

Min	Minute(s) of time	B 50

Mk	Mark	Q 101

.	.	.

.	.	.

.	.	.

B-452.9	Manually activated signals must be depicted by a legend containing the international abbreviation 'Man,' for example '(Man see note),' after the signal type (in sloping type if associated with a floating aid). A note should be inserted to describe the type of signal, activation method, channel/frequency, and duration of signal activation; or to refer to an associated publication for details. For example:

Manually Activated Sound Signal (Man)

Horn is activated by keying the mic 5 times on
VHF-FM Ch 81. Horn will operate for 30 minutes.

or

Manually Activated Sound Signal (Man)

For activation method details, see [associated publication].

Clean Version

B-122.1

International Abbreviations

.	.	.

.	.	.

.	.	.

M

m	Medium	J 31

m	Metre(s)	B 41, P 13

m	Minute(s) of time	B 50

M	Mud	J 2

M	International Nautical mile(s)
(1852 m) or sea mile(s)	B 45, P 14

Man	Manually activated	P56, R2

Min	Minute(s) of time	B 50

Mk	Mark	Q 101

.	.	.

.	.	.

.	.	.

B-452.9	Manually activated signals must be depicted by a legend containing the international abbreviation 'Man,' for example '(Man see note),' after the signal type (in sloping type if associated with a floating aid). A note should be inserted to describe the type of signal, activation method, channel/frequency, and duration of signal activation; or to refer to an associated publication for details. For example:

Manually Activated Sound Signal (Man)

Horn is activated by keying the mic 5 times on
VHF-FM Ch 81. Horn will operate for 30 minutes.

or

Manually Activated Sound Signal (Man)

For activation method details, see [associated publication].