The NCWG may also want to consider how manually activated lights should be charted.  Two options are shown below. There may be others that the working group will want to consider.

Fl.G.3s (Man see note)	Man Fl.G.3s (see note)

The notes used in combination with the additional label would be similar to the one used for sound signals.

Suggested changes to S-4 are below:

Red-Line Version

B-471.1	The type of light must only be shown on charts in a few special cases, in particular:

- Aeronautical lights (Aero), see B-476.

- Direction lights (Dir), see B-475.7 and B-475.8.

- Leading lights (Ldg), only where, because of scale, the two lights appear at a single position on the paper chart, and the leading line cannot be charted, see B-475.6.

- Manually activated lights (Man), see B-473.8.

B-473.8	Manually activated lights must be depicted by a legend containing the international abbreviation 'Man,' (in sloping type if associated with a floating aid).  For example:

Fl.G.3s (Man see note)

A note should be inserted to describe the activation method, channel/frequency, and duration of light activation; or to refer to an associated publication for details. For example:

Manually Activated Light (Man)

Light is activated by keying the mic 5 times on
VHF-FM Ch 81. Light will operate for 30 minutes.

or

Manually Activated Light (Man)

For activation method details, see [associated publication].

Clean Version

B-471.1	The type of light must only be shown on charts in a few special cases, in particular:

- Aeronautical lights (Aero), see B-476.

- Direction lights (Dir), see B-475.7 and B-475.8.

- Leading lights (Ldg), only where, because of scale, the two lights appear at a single position on the paper chart, and the leading line cannot be charted, see B-475.6.

- Manually activated lights (Man), see B-473.8.

B-473.8	Manually activated lights must be depicted by a legend containing the international abbreviation 'Man,' (in sloping type if associated with a floating aid).  For example:

Fl.G.3s (Man see note)

A note should be inserted to describe the activation method, channel/frequency, and duration of light activation; or to refer to an associated publication for details. For example:

Manually Activated Light (Man)

Light is activated by keying the mic 5 times on
VHF-FM Ch 81. Light will operate for 30 minutes.

or

Manually Activated Light (Man)

For activation method details, see [associated publication].