## CSPCWG2- 8.1C

Suggested new principles for M-4:

For coincident limits (including boundaries) the following principles apply:

- The limit symbol (line) portraying the area which is considered to be potentially the most dangerous to navigation (usually bounding permanent physical obstructions) has priority, with other limits being broken accordingly.  Restrictive limits have precedence over non-restrictive limits. Subsequently, the hierarchy is: black, magenta, green, other.

- The graticule may be broken for limits.

- All limits should be portrayed in their true location, but may be offset for clarity.

- A tint band may be added for emphasis or clarity when required.

- Tint bands must be of the same colour as the limit they emphasize.

- Where a limit symbol is broken for coincident limits, any supplementary tint band should continue unbroken along the appropriate side of the limit line.

- Bolder and longer dashes (or T shaped dashes) should be used to emphasize areas associated with routeing measures.

- Legends may be added within areas as necessary to improve clarity.

- Legends alongside limits must be placed on the inside of the limit and should not be inverted.

- The coastline and depth contours must not be broken for any maritime limit that is coincident with it.  In such cases, the limit may be offset, or information describing this fact may be included in a chart note or associated nautical publication.

- For multi-feature limits, see B-439.6.