CSPCWG 2-INF 2 ANNEX B

B-445.8	Wind turbines are generally tall, multi-bladed structures, usually with two or three blades, often visible over long distances. Their purpose is to generate electricity for large communities, or to feed a national grid. They are often in groups (known as wind farms) and may be sited on-shore (see B-374.6). Individual wind turbines must be shown by the symbol:

IL 5.1

If a navigational light is attached to the wind turbine, a flare should be added to the base, and the light description placed alongside. Where vessels may navigate close to the structure, it is appropriate to show the minimum clearance height under the blade, using symbol ID 20.

B-445.9	Wind farms may be shown by groups of wind turbines in their actual positions (if scale and available information permits), or by a maritime limit with the centred symbol:

The symbol IN 1.1 (black maritime limit implying permanent physical obstructions) should normally be used for the limit of a wind farm:

IL 5.2

However, this should be replaced by IN 2.1 or 2.2 as appropriate, where restrictions on navigation apply, eg:

IL 5.2

Note: Individual wind turbines which have navigational lights attached should normally be charted, even within a wind farm, if scale permits.

B-445.10	Underwater turbines, for generating electricity from tidal currents, must be represented:

IL 24

Where the depth of water over the turbine is known, it may be inserted within the danger circle. The rules for blue tint, swept and safe clearance depths must be applied as for wrecks and other obstructions (see B-415 and 422), eg:

Where part of the structure is above water, and marked (e.g. with a beacon or light), the appropriate symbols must be used. On small scale charts, where it may not be practicable to show the danger circle, the legend ‘Underwater Turbine’ should be used, eg:

B-445.11	Current Farm (or Turbine Field). Where groups of underwater turbines exist they should preferably be charted individually. Where scale or available information does not permit this, then the symbol IN 1.1 (black maritime limit implying permanent physical obstructions) should normally be used for the limit of a current farm:

However, this should be replaced by IN 2.1 or 2.2 as appropriate, where restrictions on navigation apply. A legend should be inserted within the boundary, eg: