## Slide 1: Satellite Derived Bathymetry GEBCO Cookbook
Derrick R. Peyton

## Slide 2: Overview
Principles
6 Steps to SDB
Canadian case study
Future work

## Slide 3: Principles

## Slide 4: Principles / Pretty
IR
Bottom return
LIDAR
Atmospheric attenuation
Sun glint
Blue Green
Seabed scattering
IR/Red: do not penetrate through water - reflected
Attenuation through water is proportional to depth
Green and Blue are attenuated in different proportions
Notes: Contains animation on click

## Slide 5: Principle / Text
Spectral range penetrating seawater typically between 350nm (UV) and 700nm (red) with following characteristic:
  Exponential attenuation of radiance is a function of depth and wavelength
  This principle is the base for depth estimation
To simplify, depth can be determined with an equation where M, N and L are empirically determined

## Slide 6: Required Data
Multispectral sensor
  Landsat 8 (free at http://earthexplorer.usgs.gov/), 30m resolution
  World view (Digital Globe), 1.85m multispectral resolution
  Spot (CNES), 6m multispectral resolution
Colour bands required:
  Blue
  Green
  Infra Red
Benchmark Data: existing bathymetry to be used to determine the M and N factors = Vertical Referencing

## Slide 7: Steps 1-6
Step 1 Acquire Satellite Imagery
Step 2 Satellite Image Processing
Step 3 Raster Calculator = Vsat = { ln(blue) / ln(green) }
Step 4 Benchmark using mbes or lidar or existing chart
determine M, N and L using least squares
Step 5 Raster Calculator to calculate SDB Depths
Step 6 Check

## Slide 8: Steps 1 Acquire Satellite Imagery

## Slide 9
Step 2 Satellite Image Processing
9
“Bad” scan lines

## Slide 10
Example: April vs. May image (2015)
>> Turbidity
>> Cloud Cover
10
Biological growth
Cloud cover
Real feature
Visible on both images
Step 2 Satellite Image Processing

## Slide 11: Water Separation
Using the Infra Red band, determine the threshold value for the land/water separation
Tool: ArcMap > 3D Analyst Tool bar
  Interpolate Line crossing from land into water
  Display histogram
Step 2 Satellite Image Processing

## Slide 12: Filtering
Apply low pass filter to each image band to remove random noise
  Spatial Analyst: convert to float
  Low pass filter
Crop to water areas only using the IR layer and determined water separation threshold value
Optional (generally not of use if good image)
  Glint/cloud correction
  In practice does not make a difference with images free of cloud cover
Step 2 Satellite Image Processing

## Slide 13: Apply Bathymetry Algorithm
Compute a new raster
Find a subset area within the benchmark data where computed raster and existing bathy are matching (= free of “fake” depths due to turbidities etc.)
Compute the M, N and L coefficients by statistical analysis.
Raster Value
Step 3 Raster Calculator

## Slide 14
Step 4 Benchmarking

## Slide 15
Step 5 Calculate SDB Depths

## Slide 16
Step 6 Check
Key Notes….
Make a plan
Know your data
QC

## Slide 17: Example of result – Nova SCOTIA

## Slide 18
18
Step 1 & 2 Acquire Satellite Imagery

## Slide 19
Looking for an area with good match between the known bathy and image
Use subset to compute coefficients
Satellite Extracted
Reference bathy
Step 1 & 2 Acquire Satellite Imagery
Notes: Reference bathy is LIDAR data (Hawkeye II)

## Slide 20
Formula: using Trendline, 2 degress polynomial.
Use raster calculated with same coefficient
Step 3 & 4 Raster Calculator

## Slide 21
Chart comparison
Step 5 Calculate SDB Depths

## Slide 22: Preliminary Results
Chart Comparison

## Slide 23: Preliminary Results
Comparison with LIDAR
  30m vs. 5m resolution
  2 to 3m standard deviation in depth values
Notes: There is not more detailed comparison – ideally would need a third multibeam survey to make a full comparison
Cannot compare with charted depths since depths from satellite are relative to ellipsoid – pending getting a chart datum separation model from CHS.

## Slide 24: Visible feature
Overlay with chart 4237

## Slide 25
Summary
Recap,
We took the GEBCO Cookbook approach to SDB
The process can be accomplished with little cost
There are primarily 6 steps to follow
Preliminary results from Canadian data is promising
Way forward,
Statistical comparison of SDB and Observed
Total Propagated Uncertainty to be developed (UNH)

## Slide 26
Thanks for Listening